We need antennas for ELRS modules:
- central frequency at 600 MHz with SWR<1.4
- 50 Ohm impedance,
- material electrical steel, diameter ~1.6 mm (awg 14)
- ipex/u.fl connector

For example modify Happymodel ELRS 915 Mhz Rx antena: